## Slide 1: Projection Based picking system
Team – BIT SPACE
Pratik Ahuja (160002041)
Nagasai Bharat (160002016)

## Slide 2: IDEA
Projection based picking system is order Picking System which is one of the most important tasks in modern warehouses. Projection based picking system can be employed in warehouses where the sizes of containers or drawers are small.
This new system works with a projector mounted at position appropriate to cover the entire rack of the warehouse. Cameras are installed at end of the rack so that it captures the special Tag attached at the side face of the drawers when it is opened and accordingly sends the information to the controlling system.

## Slide 3: Design of the system
The current system comprises of DLP EVM 2000 projector connected to a Raspberry Pi (RPi1). Another Raspberry Pi (RPi2) is connected with a USB Camera which identifies the April Tag ID. RPi2 sends the data to RPi1 which performs the comparison actions and projects the light on the drawer.
Cameras are installed at end of the rack so that it captures the special Tag attached at the side face of the drawers when it is opened and accordingly sends the information to the controlling system.
Excel sheets are uploaded and downloaded in a folder. The sheet contains the item name and the quantity to be picked. The projector projects a yellow blinking light on the drawer which contains the item. Individual navigates to the drawer, opens it and picks the mentioned quantity. A green light on drawer marks a successful pick. A wrong open of drawer makes the projector project a red light on the entire rack. The lists completed moves to a completed job folder and the process repeats.

## Slide 4: SCOPE
This work can be deployed in pharmaceutical and warehouses where the items are kept in small sized drawers. To locate the item is a difficult task and wastes a lot of time.
Hence our system projects the light on the drawer where the desired item is positioned. The system is scalable and can be extended in various other industries.
This system increases the efficiency of Human resource and makes the process smooth.

## Slide 5
FUTURE WORK
Based on daily orders and their counts the items can be moved to higher or lower positions, left or right such that the distance travelled is decreased.
The GUI can be made dynamic and flexible such that as per needs the GUI can be made which would then be projected on the drawers.